## Slide 1: Border Gateway Protocol (BGP) and BGP Security
Tirthankar Ghosh

## Slide 2: Border Gateway Protocol (BGP)
Based on Path Vector routing.
Network | Next Router | Path
Network IP | Next hop IP | AS_PATH

## Slide 3: Advantages
Loop prevention: Unlike distance vector, uses the whole route.
Policy routing: Check and verify policy, as all ASs are listed.

## Slide 4: Path Attributes
A path is characterized by a list of attributes.
Each attribute gives some information about the path.
Well-known attributes (BGP router should recognize) and Optional attributes (may not recognize).

## Slide 5: Well-known Path Attributes
Mandatory (must appear in route description). Example: AS_PATH, NEXT_HOP, etc.
Discretionary (not required in every message; but, if present, must be recognized by each router).

## Slide 6: Optional Path Attributes
Transitive (must be passed onto the next router).
Non-transitive (should be discarded).

## Slide 7: Types of BGP Messages

## Slide 8: BGP Messages (cont’d)
Open: To create a neighborhood relationship, a router sends an open message.
Update: Used to advertise new destinations and/or withdraw previously advertised destinations.
Keep-alive: To let neighbors know that the routers are alive, exchanged regularly.
Notification: Used when error is detected or when a router wants to close the connection.

## Slide 9: Vulnerabilities with BGP
BGP was designed and implemented with no security feature.
Several incidents over the past few years have indicated that BGP is vulnerable to different kinds of threats and failures.
One such incident occurred in 1997 when a misconfigured router advertised false optimal routes to all destinations in the Internet, attracting all traffic, and eventually got overwhelmed and crippled the Internet for a couple of hours.
In 1998 AS 8584 mistakenly announced 11357 prefixes on a particular day that did not belong to it. It led to a massive amount of misleading information spreading throughout the Internet, disrupting its operation.
Another error occurred in April 2001 when AS 15412 suddenly started originating thousands of prefixes that it did not own due to a local configuration error.

## Slide 10: Vulnerabilities (cont’d)
Unauthorized access to resources such as compromising BGP routers (commonly known as BGP speakers).
These compromised BGP speakers can advertise false AS_PATH information, with shorter and hence more attractive routes through themselves.

## Slide 11: Vulnerabilities (cont’d)
A malicious BGP speaker can claim to be the authorized owner of IP prefixes.
AS_PATH subversion occurs when a BGP speaker tries to modify the AS_PATH received from its peering BGP speaker without conforming to its local policy.
  Malicious shortening of AS_PATH to make it more attractive
  Lengthening of the path to make it unattractive

## Slide 12: Vulnerabilities (cont’d)
A probable threat can come from route aggregation technique used in BGP.
  An AS collects all BGP updates, instead of forwarding an update immediately. It then aggregates the prefixes in several updates and merges them in a single block, announcing the resulting block claiming that it owns all the prefixes in that block.
  In most of the cases there is no single AS_PATH that leads to all those prefixes.
  It is difficult to authenticate the claim of the advertising AS about the ownership of the advertised prefixes.

## Slide 13: Vulnerabilities (cont’d)
Route de-aggregation can also be misused to launch path subversion attacks.
Route de-aggregation breaks up an address block into more specific addresses with longer prefixes.
A compromised BGP speaker can advertise routes to an AS with more specific prefixes.

## Slide 14: Securing BGP
Two proposals that have come closest to implementation are Secure BGP (S-BGP) [Kent et al] and Secure-origin BGP (SoBGP) [White et al]

## Slide 15: Secure-BGP (S-BGP)
S-BGP is based on strict hierarchy of Public Key Infrastructure (PKI)
proposed to authenticate both the origin (address authentication) and the AS_PATH (route authentication).
Address authentication is signed by the owner of the prefix to authenticate that an AS is authorized to advertise the prefix.
Route authentication is signed by a BGP speaker to authenticate the AS_PATH.
The speaker signs a message consisting of the prefix, the current AS_PATH, and the AS number of the intended recipient and sends the message to all its neighbors, along with all previous route authentications of the earlier components of the AS_PATH.

## Slide 16: S-BGP (cont’d)
S-BGP imparts a very high computational cost because of a large number of signature verifications.
It is extremely difficult to establish a centralized PKI in the Internet infrastructure.
These limitations have contributed to the failure of wide scale deployment of S-BGP.

## Slide 17: So-BGP
SoBGP has also been proposed to provide a method that BGP speakers can use to validate the correctness of BGP update messages.
It uses digitally signed objects (certificates) to distribute authorization and policy:
  AS policy certificate asserts the routing policy of an AS;
  Authorization certificate asserts that an AS is authorized to advertise a particular prefix;
  Entity certificate asserts mapping between an AS identifier and its public key

## Slide 18: So-BGP (cont’d)
Authorization certificates and AS policy certificates are verified by public keys embedded in entity certificates.
Routers use topology database to validate received routes.
The implementation of So-BGP depends on the complexity of establishing a PKI hierarchy in the Internet.