## Slide 1: Layer 2 Vulnerabilities
CNA 432/532
OSI Layer Security
Dr. Tirthankar Ghosh
Courtesy: Cisco Systems, Inc.

## Slide 2: Attacks
CAM table overflow
VLAN hopping
Spanning Tree Protocol (STP) manipulation
MAC address spoofing
ARP cache poisoning
Private VLAN
DHCP starvation

## Slide 3: CAM Table
Content Address Memory (CAM) table maintains list of MAC addresses mapped to switch ports.
Switch refers to its CAM table when forwarding packets.
If an entry is not present in its CAM table, the switch broadcasts the packet through all its ports.
When a response is seen, the switch updates its CAM table.

## Slide 4: CAM Table Overflow
CAM tables are limited in size in memory.
An attacker floods the switch with fake MAC addresses to fill up the CAM table.
The switch then reverts to a hub mode.

## Slide 5: Preventing CAM Table Overflow Attack
Configure port security in the switch
  Specify number of MAC addresses in a port.
Configure dynamic port security in a switch
  Specify the maximum number of MAC addresses that can be learned in a port.

## Slide 6: VLAN Hopping Attack
Network attack where an attacker connected to a VLAN sends unauthorized traffic to another VLAN.
The traffic is tagged with a different VLAN id to which the end system belongs to.
The attacker can also behave like a switch and negotiate trunking.

## Slide 7: VLAN Hopping Attack (cont’d)
The attacker behaves like a switch by emulating the 802.1q signaling and the Dynamic Trunking Protocol (DTP) signaling.
The attacker can then become member of all VLANs.
Double tagging:
  Attacker tags the packet with two 802.1q headers.
  The first switch strips off the outer header, forwards the packet to all switch ports, including the trunk port.
  The second switch then forwards the packet to the final destination based on the VLAN id in the inner header.

## Slide 8: Preventing VLAN Hopping Attack
Use dedicated VLAN ids on the trunk port.
Disable all unused ports, place them on an unused VLAN.
Turn off Dynamic Trunking Protocol (DTP) on user ports.

## Slide 9: Spanning Tree Protocol (STP) Manipulation
STP is used in switched networks to create a loop-free topology.
One switch is identified as the root bridge, and all redundant data paths are blocked.
The attacker transmits spoofed STP packets, causing the switches to initiate STP recalculations, resulting in a forwarding path through the attacker. This becomes possible if the attacker spoofs a root bridge with high priority.

## Slide 10: Preventing STP Manipulation
Use root guard and BPDU guard enhancements.
Root guard feature is used to enforce a root bridge placement in the network.
  Limits switch ports through which STP control messages are negotiated.
  If a root-guard-enabled port receives messages with higher priority, then that port is moved to a root-inconsistent state, and no data traffic is forwarded across that port.
STP Bridge Protocol Data Unit (BPDU) Guard is designed to have a predictable active network topology.
  BPDU Guard-enabled port will become disabled on receiving a BPDU.

## Slide 11: ARP Flooding and ARP Cache Poisoning
An attacker can create a flood of spoofed ARP reply packets overflowing a switch’s ARP cache, and forcing it to the hub mode.
The attacker can poison ARP cache in a switch or other hosts by sending spoofed ARP replies.

## Slide 12: MAC Spoofing
Practically every Ethernet adapter can be reprogrammed to have any desired hardware address.
Attackers can reprogram the Ethernet adapter on a system to spoof that of another system on the network.

## Slide 13: Preventing MAC Spoofing
Enable switch port security
  Specify MAC addresses on a switch port.
Use DHCP snooping along with Dynamic ARP Inspection (DAI)
  When a spoofed ARP reply is sent, the MAC address-IP address mapping is changed in the DHCP database.
  A host that is connected to a switch port not a DHCP server port, is not trusted to send ARP replies that change the mapping.

## Slide 14: Private VLAN Attacks
Private VLANs are used to restrict communication from some ports to other ports in the same VLAN.
Isolated ports within the VLAN can communicate only with promiscuous ports.
Promiscuous ports can communicate with any port.
Attackers can bypass these restrictions by using proxy.

## Slide 15: Private VLAN Attacks (cont’d)
Attacker sends a frame to a router using the router’s MAC address as the destination MAC and the target’s IP address as the destination IP.
The router sends the packet back to the target host.
This attack is only unidirectional from the attacker to the target.
Prevention:
  Configure ACL in inside interface of the router to block packets with destination IP address as that of the inside host’s.

## Slide 16: DHCP Starvation
Sending fake DHCP requests with spoofed MAC addresses.
Setting up a rogue DHCP server to respond to new DHCP requests.
Prevention:
  Limit number of MAC addresses on switch ports.
  DHCP authentication (RFC 3118).

## Slide 17: IEEE 802.1x
Standard for using the Extensible Authentication Protocol (EAP) over wired and wireless networks.
Has three components:
  Supplicant: the client who needs to be authenticated
  Authenticator: to whom the client authenticates
  Authentication server (RADIUS, TACACS)

## Slide 18: Vulnerabilities with EAP
Man-in-the-middle attack on a wireless network
  The attacker sends an EAP success message to the supplicant that is forged so as to come from the authenticator.
  The state machines in both the authenticator and the supplicant change to authenticated state.
Session hijacking
  Attacker sends MAC-spoofed disassociate message to the supplicant as if it’s coming from the authenticator.
  The supplicant gets disassociated, but the authenticator is still in the authenticated state.
  The attacker now gains access to the network by forging the disassociated supplicant’s MAC address.

## Slide 19: Protected EAP (PEAP)
Establishes TLS session between supplicant and authentication server.